## Slide 1
LC100 NPI
2-Channel HD Recorder and Streaming Media Processor

## Slide 2
Recording
Stream
Store
Produce
Switch
Overview
All-in-One Video Solution
Recording
Stream
Store
Micro-Production
Switch

## Slide 3
LC100
Multi-channel Video Mixing | 2 Video Source | 4 Video Source
Recording Modes | 1 mixed + 2 individual original | 1 mixed + 4 individual original
Video In | HDMI*2 (one HDMI 2.0) 3G-SDI*1 IP Video Source*2 USB Camera*1 | HDMI*4 IP Video Source*3
Audio In | XLR*2 3.5mm Line In*1 HDMI Audio*2 SDI Audio*2 USB Audio*1 IP Audio*2 | 3.5mm & Line In*4 (Unblance, Stereo) HDMI Audio*4 IP Audio
Video Out | HDMI out*2 HDMI Pass Through*1 (up to 4K) | HDMI*2
LCM | Yes, OSD Menu | NA
Built-in HD | Built-in SATA 2TB HDD | Standard: SATA 1TB HDD Optional: SATA 2TB HDD
Streaming | RTSP / RTP / RTMP / RTMPS / SRT | RTSP / RTP / RTMP / RTMPS
LC200
*Only available in special regions
Product Family

## Slide 4
Record and Stream
Source/Layout Switch
Power/Standby/Reboot
USB 3.0/USB 2.0
Control Knob
Status Screen
Built-in 2TB HDD
Product I/O
LC100 Front View

## Slide 5
HDMI/SDI IN 1
HDMI Pass-Through (Direct Output from
HDMI IN 1)
Program Out
Multi-view Onboard Director Out
USB 3.0
Ethernet
XLR Balanced Audio
Line In & Line Out
HDMI/SDI IN 2
Product I/O
LC100 Back View

## Slide 6
Onboard GUI Director
Live control is incorporated into the device. Connect an HDMI screen to the LC100 to access the intuitive GUI. Sessions can be produced live or scheduled in advance.
Live Pre-defined Scenes for Switching
Build layout scenes that incorporate a variety of visual elements include split screen video, picture-in-picture, title/logo overlays, and background images. Activate and change layouts with the click of a mouse.
Program &
ISO Recording
The LC100 records the mixed program-out video and captures two video inputs with independent audio. This simplifies media archiving and post-production.
Key Features-1

## Slide 7
Deployment Tool for Remote Central Management
The Lumens deployment software enables control, management, and administration of multiple LC100 units on the network. Administrators can remotely monitor device status, saving time and reducing costs.
Intermission Scene
Need a break time during the streaming session? Hit the coffee mark to display the break time page. Users can upload their own designed intermission screen
Key Features-2

## Slide 8
Lumens LC100
B&H Price (USD$) | $3,250 | $1,695 | $4790
Recording Resolution and FPS | 1080p 60fps | 1080p 60fps | 1080p 30fps
Recording mode | 1080p60: 3 files | 1080p60: 1 files | 1080p60: 1 files
PTZ Camera Control | Yes | NA | NA
Video In | HDMI*2 (HDMI 2.0 *1) 3G-SDI *2 IP Video Source *2 USB 3.0 *1 | 12G-SDI *1 HDMI *1 IP Stream *1 | HDMI *3 3G-SDI *1 (Optional)
HDMI pass-through | Yes | Yes | NA
Audio In | XLR *2 3.5mm Stereo*1 USB Audio *1 IP Audio from RTSP *2 | XLR *2 RCA (L/R) *1 USB *1 IP Audio from RTSP or SRT *2 | Audio In *2
Storage | Built-in SATA 2TB HDD External: USB 3.0 Storage | SD Card (Up to 512 GB) M.2 (SATA) SSD | Internal 80G SSD
Extension Remote Control Panel | Yes, LC-RC01, up to 30 meter USB extension | USB status light (optional) | Yes, Optional
Warranty | 5-year | 1-year | 3-year
Epiphan Pearl Nano
Extron SMP351
Competitive Products

## Slide 9
*We provide two Standard remote control panels.
Lumens LC-RC01 remote control panel, a wall plate for the LC100 to control the live streaming, recording, and video file saving options. The panel provides three macro functions that can remotely switch the scene and control the cameras preset. The LC-RC01 can be extended to 30 meters through a Cat 5e cable. Equipped with a USB port, it supports USB flash drives to record or backup video files.
LC-RC01 Remote Control Panel
Accessory

## Slide 10
How to Control?
Remote Control Panel
LC-RC01
Onboard GUI
with Wireless mouse
Web Online Director
USB Keypad
RS-232
RS-485
1
2
3
4
5
LC100 provide below control interface.
Remote control panel: LC-RC01
Onboard GUI Interface: Use mouse and keyboard to operate the GUI from Multiview HDMI out.
Online Director: Webpage
USB or wireless keypad: one click to record
RS-232, RS-485, TCP/IP control: Provide command for supporting third-party controller, like Crestron, Extron controllers.

## Slide 11
External USB Storage (up to XX TB)
Exchange SATA Hard Disk Drive (up to XX TB)
2.5”
3.5”
Built-in 2TB
You can install your data in the build in 2TB storage, or if the build in 2TB is too small you can exchange to bigger HaerdDisk, or you can add one external USB storage.
3 Local Storage Options
How to Backup Data (1)?

## Slide 12
FTP
NAS
The built-in storage space is limited, and the video files must be uploaded to the network storage space automatically, for the user to backup and manage.
Network Storage
How to Backup Data (2)?
You can buckup to LMS (learning
management systems) like Panopto, Kaltura, and Opencast.
You can upload to NAS or FTP/SFTP server

## Slide 13
Software
Accessory
Deployment Tool
Camera
Remote Control Panel
Media Processor
LC100 is a powerful all-in-one Media Processor with HDMI, SDI USB, and Ethernet inputs. The various AV inputs make it easier to connect with all ranges of Lumens cameras. LC100 is compatible with Lumens LC-RC01 Remote Control Panel and Lumens Deployment Tool software. It allows you to remotely manage and control LC100 devices.
Lumens Products
Integration

## Slide 14
Broadcasting Software
Streaming Platform
Stream Deck
Video Content Management
LC100 successfully integrates with major content management systems, popular streaming platforms, broadcasting software, and stream deck. It provides users with more flexible options to use LC100 with their desired platforms.
Third Party Partners
Integration